## Slide 1: Digital Twin of Power Converter Systems Identification and Optimization for Reliability
Fernando Troya
Dr. Ing. Martin Votava
03-03-2025

## Slide 2: Outline
Introduction & Motivation
Review of Identification Methods
Methodology
Results
Conclusion

## Slide 3: Motivation
Increase in EV chargers
Higher power charger trend
Increased converter usage
Need for robust reliability and health monitoring.
Need for accurate thermal models to maximize safe converter usage.
Real time embedded deployment of monitoring
EV charger Trends
EV charger Trends:
Fig.1 EV charger Trends [1]
Fast charging
Introduction
Review
Methodology
Results

## Slide 4: Introduction to Digital Twins
The DT processes real-time sensor data to adapt a twin model of a process.
Thermal 'constants' drift due to aging; the Digital Twin adaptively mirrors the physical module's degradation.
Fig.2 Digital twin Topology [2]
Introduction
Review
Methodology
Results
Kuprat et al. Dynamic mode decomposition with control [2]
Notes: Provide insight into non measurable variables

## Slide 5: Models
Common modeling approaches include Lumped Parameter Thermal Networks (LPTN), FEA, and Data-Driven models.
Fig.3 Cauer Network [2]
Fig.4 Semiconductor Heating FEA[3]
Fig.5 Data driven modelling [4]
Introduction
Review
Methodology
Results
Notes: Lump, represent thermal res and cap properties as elect RC
FEA simulates heat diffusion PDE
Data driven trains models with big datasets

## Slide 6: Cauer network Parameter identification
A reliable computationally light identification method is required
Easy Implementation in embedded systems
Computationally light
Easy interpretation
Over-simplifies dynamics
Parameters are not measurable
Thermal parameters are fixed
Advantages
Disadvantages
Network layers represent physical layers.
Node Temperatures represent average physical temperatures
Variation in thermal parameters correlated with physical degradation.
Monitoring Principle
Fig.3 Cauer Network [2]
Introduction
Review
Methodology
Results
Kuprat et al. Dynamic mode decomposition with control [2]

## Slide 7: Experimental Validation
Experimental Validation Strategy: EKF, PSO and a data driven apporach will be analyze for feasability
(PSO & EKF): Validated on single-chip self-heating data to identify localized Cauer parameters.
Data-Driven (H-DMD): Validated on a dual-chip setup with cycling power to capture complex thermal cross-coupling.
.
Fig. 6 Experiment A self heat [†]
Fig. 7 Experiment B self heat [†]
Fig. 8 Experiment C cycling [†]
Introduction
Review
Methodology
Results
P2
T2
P1
T1

## Slide 8: EKF
Good for one step prediction
Can not separate the fast and slow dynamics
Fig. 9 EKF scheme
adapted model
Initial guess
Fig. 10 EKF convergence
Fig. 11 EKF validation
Introduction
Review
Methodology
Results
adapted model
Initial guess

## Slide 9: PSO
Global Identification: Optimizes and without Jacobian requirements.
Real-time Constraint: Execution limited to 3 iterations per window.
Swarm Diversity: 40% re-randomization of worst-performing particles.
Recursive Warm-start
Fig. 12 Online PSO [*]
Introduction
Review
Methodology
Results
Notes: Is usually offline
Global stochastic
Local minima stuck
Simulation rankings

## Slide 10: PSO accuracy
PSO Identification Accuracy
Validation: Tested on single-chip self-heating
Steady-State Precision: Achieves during stable operating points
Transient Dynamics:error "spikes" occur during high events
Convergence: Rapid parameter stabilization within the first 3–5 windows
Initial guess
Adapted model
Fig. 13 PSO Convergence
Fig. 14 PSO Validation
Introduction
Review
Methodology
Results
Adapted model
Initial guess

## Slide 11: Data Driven DMD
Goal: Define a system
We need to find a matrix that advances the state respecting the dynamics
Introduction
Review
Methodology
Results
Based: Proctor et al. Dynamic mode decomposition with control [5]
Notes: We need to capture the slow and fast dynamics, we augment the state-> time embeddings
The blocks have repeating patterns in the heating dynamics and lags

## Slide 12: Data Driven DMD
Introduction
Review
Methodology
Results
Based: Proctor et al. Dynamic mode decomposition with control [5]
Fig. 15 Hankel DMD [*]
Goal: Define a system
We need to find a matrix that advances the state respecting the dynamics
Notes: We need to capture the slow and fast dynamics, we augment the state-> time embeddings
The blocks have repeating patterns in the heating dynamics and lags

## Slide 13: Data Driven DMD
Fig. 15 Hankel DMD [*]
Computationally expensive
Fig. 16 DMD DT Scheme [*]
Introduction
Review
Methodology
Results
Based: Proctor et al. Dynamic mode decomposition with control [5]
Goal: Define a system
Notes: We need to capture the slow and fast dynamics, we augment the state-> time embeddings
The blocks have repeating patterns in the heating dynamics and lags

## Slide 14: Data Driven DMD
Fig. 15 Hankel DMD [*]
Repeating patterns
Computationally expensive
Introduction
Review
Methodology
Results
Based: Proctor et al. Dynamic mode decomposition with control [5]
Goal: Define a system
Fig. 16 DMD DT Scheme [*]
Notes: We need to capture the slow and fast dynamics, we augment the state-> time embeddings
The blocks have repeating patterns in the heating dynamics and lags

## Slide 15: Data Driven DMD
Goal: define a system
Computationally expensive
Fig.17 SVD psudo-inversion [*]
Introduction
Review
Methodology
Results
Based: Proctor et al. Dynamic mode decomposition with control [5]
Fig. 16 DMD DT Scheme [*]
Notes: Break down omega aug into its principal components
Truncate the components with highest weight/energy
Aproximate omega
Invert omega

## Slide 16: Data Driven DMD
Goal: Adapt a system
Fig. 18 Online DMD RLS [*]
Introduction
Review
Methodology
Results
Based: Zhang et al. Online dynamic mode decomposition for time-varying systems[6]
Fig. 16 DMD DT Scheme [*]
Notes: RLS for matrices
nstead of storing the whole history, we only store two compact matrices: the current operator and the inverse covariance P
Sherman-Morrison formula to update the inverse cov P, basically no need to update P and invert again, can directly update the inverse
($\rho$): Emphasize that $\rho$ (e.g., $0.9999$)

## Slide 17: DMD Results
Initial guess
Adapted model
Fig. 19 Online DMD convergence
Fig. 20 DMD DT Validation
Introduction
Review
Methodology
Results
Adapted model
Initial model

## Slide 18: Summary
Method | Primary Strength | Main Challenge | Best Use Case
Online PSO (with 40% Reset) | Global Search: Excellent at finding parameters in non-convex spaces without needing a gradient/Jacobian. | Stochastic: Computationally heavier per iteration; requires windowed data for convergence. | Initial Calibration: Best for finding the baseline "Golden Model" Cauer parameters offline or during startup.
Augmented EKF (Log-Space) | Recursive Efficiency: Updates at every sample; provides a covariance matrix (uncertainty) for health monitoring. | Local Convergence: Requires accurate initial guesses; sensitive to process noise tuning. | Continuous Tracking: Ideal for real-time monitoring of parameter drift (aging) during operation.
Hankel-DMD (Reduced Order) | Temporal Memory: Captures complex diffusion dynamics (4-mode) without needing a manual RC structure. | Data Driven: Lacks direct physical layer interpretability. | High-Speed Control: Best for fast Tj prediction in complex multi-chip modules with cross-heating.
Conclusion: The ideal method depends on the module complexity, and desired application, but it should be sensitive to both fast and slow thermal constants.

## Slide 19: Future Work
Extend the Digital Twin to include heatsink temperature-based adaptation.
Enhance the physical interpretability of DMD-derived thermal parameters.
Fig. 20 Future work scheme [*]

## Slide 20: References
[1] IEA, “Global stock of public charging points by speed, 2018-2024 – Charts – Data & Statistics.” Accessed: Dec. 26, 2025. [Online]. Available: https://www.iea.org/data-and-statistics/charts/global-stock-of-public-charging-points-by-speed-2018-2024
[2] J. Kuprat, K. Debbadi, J. Schaumburg, M. Liserre, and M. Langwasser, “Thermal Digital Twin of Power Electronics Modules for Online Thermal Parameter Identification,” IEEE J. Emerg. Sel. Topics Power Electron., vol. 12, no. 1, pp. 1020–1029, Feb. 2024. doi: 10.1109/JESTPE.2023.3328219.
[3] COMSOL, “Thermal Analysis of a Bipolar Transistor.” Accessed: Dec. 29, 2025. [Online]. Available: https://www.comsol.com/model/thermal-analysis-of-a-bipolar-transistor-19701
[4] Y. Tang et al., “Physics-Informed Intelligent Thermal Model for SiC Power Modules With High Generalization,” IEEE Trans. Power Electron., vol. 40, no. 10, pp. 14459–14477, Oct. 2025. doi: 10.1109/TPEL.2025.3577241.
[5] J. L. Proctor, S. L. Brunton, and J. N. Kutz, “Dynamic mode decomposition with control,” Sep. 2014, arXiv: 1409.6358. doi: 10.48550/arXiv.1409.6358.
[6] H. Zhang, C. W. Rowley, E. A. Deem, and L. N. Cattafesta, “Online dynamic mode decomposition for time-varying systems,” Jul. 2017, arXiv: 1707.02876. doi: 10.48550/arXiv.1707.02876.
[7] M. Votava, K. Debbadi, Y. Pascal, and M. Liserre, “Multi-step Least Squares Algorithm for Thermal Characterization Based on Mission Profile,” in 2024 IEEE Applied Power Electronics Conference and Exposition (APEC), Feb. 2024, pp. 1566–1573. doi: 10.1109/APEC48139.2024.10509492.

## Slide 21: Acknowledgement
[†] Experimental Validation: All raw thermal experimental data for the modules was graciously provided by Dr. Martin Votava
[*] Technical Visualizations Note (diagrams):
Some of the diagrams and system architecture illustrations presented in this seminar were designed by the author and rendered using Generative AI (Gemini 3 Flash/Nano Banana 2). All visual logic, mathematical notations, and block structures are derived directly from the underlying CauerEKF and DMDc Python implementation to ensure technical fidelity.